## Slide 1
PointNet++ Attention Enhancement
ModelNet40 and 3D MNIST Classification Study
JIANG Yuchen 59617983
PointNet++ Attention Enhancement

## Slide 2
Context
Project Scope
Two parallel threads shaped the final outcome
Architecture Track
Start from PointNet++ SSG as the baseline.
Explore SE blocks, local attention pooling, and cross-level fusion.
Diagnose the failure of attention v1 and redesign it into attention v2.
Outcome
A stable Mac-compatible codebase.
A corrected attention model that is much stronger than the first attempt.
A second-dataset evaluation pipeline on 3D MNIST.
PointNet++ Attention Enhancement

## Slide 3
Architecture
Baseline Method
PointNet++ SSG classification pipeline
SA1
512 points
radius 0.2
32 neighbors
64 -> 64 -> 128
SA2
128 points
radius 0.4
64 neighbors
128 -> 128 -> 256
SA3
Global grouping
256 -> 512 -> 1024
single global descriptor
Classifier
1024 -> 512 -> 256 -> class
standard PointNet++ SSG head
This baseline is already strong on ModelNet40, so the real target is not only to beat the original paper, but to beat a strong local retrain.
PointNet++ Attention Enhancement

## Slide 4
Methods
Optimization Path
What each model variant tried to improve
Baseline
Pure PointNet++ SSG.
Strong local hierarchy.
Reference model for all later comparisons.
SE Version
Add channel attention after SA1 and SA2.
Deepen the classifier.
Goal: better channel discrimination and class balance.
Attention v1
Replace max pooling with local attention pooling.
Fuse l1, l2, l3 with cross-level attention.
Goal: richer local weighting and multi-scale fusion.
Attention v2
Masked local attention.
Hybrid attention + max pooling.
CLS-token fusion plus global residual.
Stronger nonlinear classifier.
PointNet++ Attention Enhancement

## Slide 5
SE
Why SE Was Introduced
Channel recalibration plus a stronger head
SE stands for Squeeze-and-Excitation. The block globally averages each feature channel, learns a channel importance vector, and rescales the original features.
The intuition is simple: not every feature channel contributes equally to classification, so the network should emphasize informative channels and suppress weaker ones.
91.976%
SE best instance acc
89.526%
SE best class acc
Result: SE improved class accuracy over baseline, but it did not surpass baseline on instance accuracy.
PointNet++ Attention Enhancement

## Slide 6
Diagnosis
Why Attention v1 Failed
The first attention design was conceptually interesting but technically flawed
Problem 1: invalid local attention
PointNet++ radius grouping duplicates the first valid neighbor when padding.
This is safe for max pooling.
It is not safe for softmax attention because fake duplicates collect probability mass.
Each hierarchy level was reduced to a single mean-pooled token.
The attended tokens were then averaged again.
Too much structure was discarded before attention could help.
Problem 3: weak classifier
The post-fusion classifier behaved too close to a shallow linear head.
There was not enough nonlinear capacity to exploit the fused representation.
91.392% / 86.231%
Best ModelNet40 result of attention v1
PointNet++ Attention Enhancement
Problem 2: over-compressed fusion

## Slide 7
attn-v2
Attention v2 Design
A corrected architecture, not just a larger one
Masked local attention
Return explicit validity masks from grouping.
Normalize softmax only over valid neighbors.
Hybrid local pooling
Fuse attention pooling with max pooling.
Keep PointNet++ robustness while adding learnable weighting.
Cross-level fusion
Use mean and max summaries.
Add a CLS token and a global residual path from l3.
Classifier
Wider nonlinear head.
512 -> 256 -> 128 -> class.
Result: attention v2 recovered most of the performance lost by attention v1 and strongly improved class balance.
PointNet++ Attention Enhancement

## Slide 8
Pipeline
Engineering and Logging Infrastructure
The project became reproducible, not just runnable
Platform support
Automatic MPS / CUDA / CPU device selection.
Safer index handling and masking on Apple Silicon.
Conservative worker settings for macOS.
Dataset-aware training
A unified train script now supports ModelNet40, ModelNet10, and 3D MNIST.
The evaluation script can reuse run configuration automatically.
Persistent experiment records
run_config.json for exact arguments and environment.
metrics.csv for per-epoch curves.
summary.json for the best final result.
Exact code snapshots copied into each run directory.
PointNet++ Attention Enhancement

## Slide 9
Evaluation
Experimental Setup and Metrics
What was measured and how
Metrics
Instance accuracy: percentage of correctly classified test samples.
Class accuracy: average of per-class accuracies. Train accuracy, learning rate, and global step logged per epoch.
PointNet++ Attention Enhancement
Setup
Adam Optimizer,
initial learning rate 0.001,
StepLR scheduling,
no normal vector

## Slide 10
Results
ModelNet40 Results
The local baseline remains the strongest top-line model
Model | Best Inst. | Best Class | Best Epoch
Baseline | 92.459% | 89.175% | 68
SE | 91.976% | 89.526% | 92
attn-v1 | 91.392% | 86.231% | 88
attn-v2 | 92.056% | 89.597% | 100
Chart: 
| Baseline | SE | attn-v1 | attn-v2
Instance Accuracy | 92.459 | 91.976 | 91.392 | 92.056
Class Accuracy | 89.175 | 89.626 | 86.231 | 89.597
Attention v2 is a strong repair over attention v1, but it still trails the local baseline by 0.403 points in instance accuracy.
PointNet++ Attention Enhancement

## Slide 11
Paper
Comparison with the PointNet++ Paper
The local retrain is the real benchmark
Method | Features | Instance Acc.
PointNet++ paper | XYZ only | 90.7%
Local baseline | XYZ only | 92.459%
attn-v2 | XYZ only | 92.056%
+1.759
Baseline vs paper XYZ
+1.357
attn-v2 vs paper XYZ
The codebase and training recipe already outperform the original 2017 paper result. That is why the local baseline, not the paper alone, is the correct target for judging the new method.
PointNet++ Attention Enhancement

## Slide 12
Dataset
3D MNIST Integration
A practical second dataset for cross-dataset validation
Why 3D MNIST
It was available locally as point-cloud-oriented HDF5 files.
It could be integrated much faster than ScanObjectNN or raw ShapeNetCore.
It still provides a real second 3D classification task.
What the loader does
Read HDF5 groups with points, normals, and labels.
Sample each object down to 1024 points.
Normalize XYZ and optionally concatenate normals.
Dataset properties
Train: 5000 samples.
Test: 1000 samples.
Classes: 10.
Average raw point count above 20k.
PointNet++ Attention Enhancement

## Slide 13
Results
3D MNIST Results
A clean same-setting comparison between baseline and attn-v2
98.611%
Baseline best instance acc
98.623%
Baseline best class acc
98.710%
attn-v2 best instance acc
+0.099 vs baseline
98.939%
attn-v2 best class acc
+0.316 vs baseline
Chart: 
| 1 | 5 | 10 | 20 | 40 | 60 | 80 | 100
Baseline | 71.726 | 87.599 | 83.631 | 94.246 | 96.627 | 98.611 | 98.016 | 98.611
attn-v2 | 37.798 | 89.683 | 89.583 | 95.139 | 97.718 | 98.313 | 98.115 | 98.512
Baseline learns faster at the start.
attn-v2 catches up gradually and ends slightly stronger on both best metrics.
The gain is small, but it is consistent and class-aware.
PointNet++ Attention Enhancement

## Slide 14
Limitations
Drawbacks and Future Work
The final result is credible because the limitations are explicit
Drawbacks
attn-v2 does not beat the strongest local baseline on ModelNet40 instance accuracy.
The parameter count is very high: 5.95M vs 1.48M for baseline.
No full ablation and no multi-seed evaluation were run.
3D MNIST is useful but not a strong realism benchmark.
Recommended next steps
Ablate masked attention, hybrid pooling, cross-level fusion, and classifier depth separately.
Reduce the late-stage parameter cost in attention v2.
Evaluate on a stronger second dataset such as ScanObjectNN.
PointNet++ Attention Enhancement

## Slide 15
Takeaway
Final Conclusion
A balanced result is still a strong research outcome
The project delivered a stable Apple Silicon pipeline, a corrected attention model, and a reusable cross-dataset evaluation workflow.
Attention v2 is clearly better than attention v1 and shows modest promise on a second dataset
PointNet++ Attention Enhancement

## Slide 16
Thank you
PointNet++ Attention Enhancement